## Slide 1
EMG processing
Experiment paradigm

## Slide 2
Center Hit
Go Cue
Target Hit
Center On
A monkey was trained to perform a center-out task by contracting wrist muscles on left hand
Since his hand was put inside the small box, the contraction is considered as isometric
Forces were obtained by a load cell and mapped to a cursor on the screen
Experiment paradigm
0
180
135
90
45
-135
-90
-45
data[‘target_dir’]
data[‘trial_start’]
data[‘trial_gocue’]
data[‘trial_end’]

## Slide 3
EMG processing
Signal acquisition

## Slide 4
Flexor carpi radialis (FCR)
Flexor carpi ulnaris (FCU)
Extensor carpi ulnaris (ECU)
Extensor carpi radialis (ECR)
R
U
Radial deviation
Ulnar deviation
Extension
Flexion
Signal acquisition pathway
multi-ch pre-amplifier and BP filters
Analog-digital converter
fs = 2000 Hz
Computer
Multi channel fine wire electrodes
Blacrosk Cerebus
+
-
Implantable stainless steel wires
Fixed with suture

## Slide 5
Computational task 1
Estimating wrist movement directions from EMGs

## Slide 6
FCU
FCR
ECU
ECR
Trial separation and basic observations
Trials are aligned with the Go-cue event
t = 0 at Go-cue
Can we estimate which direction the monkey was moving the cursor to with EMGs inside a specific short window?
Can be done with a classifier
Try the window between Go-cue and Go-cue + 500 msec

## Slide 7
Form a spatial-temporal vector for each trial from down-sampled EMGs
Trials
Trials
Reshape
Original data
In this case, there are 294 trials. The number of muscles N = 4. The length for each trial T = 0.5 s (10 samples)
Reshaped data
For each trial, the 10*4 EMG data array is converted into a vector with 40 dimensions

## Slide 8
Train a MLP classifier
Multilayer perceptron
Input data:
EMG vectors
Input dim:
T*40
Output data:
Class labels
Output size:
8
Splitting training and testing data. 50% trials are held out for testing
Training an MLP classifier with the training data
Here we will use packages in sklearn to build and test an 8-class classifier

## Slide 9
Train a MLP classifier
The results on testing set is shown below. The overall accuracy is 97.2%

## Slide 10
Computational task 2
Predicting forces from EMGs

## Slide 11
Filter length: 250 ms, or 5 lags
EMG envelops
Wiener filter
Forces
Fx
Fy
Muscles
Time
Time
Predicting forces from EMG envelops using a Wiener filter-based decoder
2.5 | 1.3 | 2.5 | 6.8 | 7.4 | 2.3 | 8.8 | 8.3 | 9.2 | 7.1
7.4 | 2.3 | 8.8 | 8.3 | 9.2 | 7.1 | 8.8 | 8.3 | 2.3 | 8.8
8.8 | 8.3 | 2.3 | 8.8 | 7.4 | 2.3 | 8.8 | 8.3 | 9.2 | 7.1
2.3 | 8.8 | 7.4 | 2.3 | 8.8 | 8.3 | 9.2 | 7.1 | 8.8 | 8.3
11 | 23 | 12 | 2.6 | 8.7 | 22 | 36 | 1.6 | 2.7 | 56
8.7 | 22 | 36 | 12 | 2.6 | 8.7 | 8.3 | 12 | 2.6 | 8.7

## Slide 12
Predicting forces from EMG envelops using a Wiener filter-based decoder
R2 for Fx: 0.803
R2 for Fy: 0.927
Actual
Predicted
Forces are predicted from the EMGs continuously, and no trial information is used.
Data during the first 10 minutes (~12000 samples) are used for training.
Data during the last 10 minutes are used for decoder performance testing.
On testing set
Using r2_score in sklearn.metrics to calculate the decoding accuracy